## Slide 1: Applications in Embedded Environment
March 8, 2016
Cosmin Stoica – Automotive OS Team SW ENGINEER
Embedded Programming Workshop

## Slide 2: Info
Internet Access: Freescale Guest
  Username and Password available on papers
Workshop files:
  www.nxp.com/linuxembeddedchallenge
  http://www.nxp.com/linuxembeddedchallenge -> Categories -> Workshop Files

## Slide 3: UDOO & ArduinO

## Slide 4: Arduino
Arduino is:
  Open-source physical computing platform
  Inexpensive
  Cross-platform
  Simple, clear programming environment
  Open source and extensible software
  Open source and extensible hardware

## Slide 5: Arduino Sketch & Arduino IDE
Global Variables
setup()
loop()
Declare variables at top
Initialize
Running
Reset Button Pressed

## Slide 6: Arduino & UDOO

## Slide 7: UDOO GPIO Pinout
most of the GPIOs available on
external pin headers shared by
I.MX and Atmel SAM3X8E
Pin mode:
  INPUT
  OUTPUT
Both processors can control all digital
external pins
Atmel SAM3X8E - Arduino applications
I.MX processor – Linux/Android
http://www.udoo.org/tutorial/linux-gpio-manipulation/

## Slide 8: SAM3x8E GPI/Os management
Arduino Programming Language
Set the direction of pin (setup):
  pinMode(<pin_number>, INPUT);
  pinMode(<pin_number>, OUPUT);
Pin states:
  INPUT: digitalRead(<pin_number>)
  OUPUT: digitalWrite(<pin_number>, LOW/HIGH)
  Note: analogRead/analogWrite for PWM
  Details about Arduino Language

## Slide 9: i.MX6 GPI/O Management
External PINS can be handled as:
  GPIO
  I2C, SPI, PWMs output, UART etc…
GPIO:
  managed by the kernel
  accessible using /sys/class/gpio
    direction (in/out)
    value (0/1)
cat /sys/class/gpio/gpioXX/direction
echo out/in > /sys/class/gpio/gpioXX/direction
cat /sys/class/gpio/gpioXX/value
echo 0/1 > /sys/class/gpio/gpioXX/value

## Slide 10: GPIOs Warnings
UDOO I/O pins are 3.3V only compliant!

## Slide 11: Programming LED Blink on Arduino IDE
Open Arduino IDE
  setup() and loop ()
API:
  delay
  pinMode
  digitalWrite
  digitalRead
Connect the LED
  Shorter leg to ground
  Longer leg to PIN13
TODO: Blink the LED
Extra: Vary the brightness of the LED

## Slide 12: Programming UDOO Arduino Processor from External PC
A working SD Card
Close the serial monitor
J18 jumper should be unplugged.
Allow the communication between PC and
the programming port of the SAM3X
Serial cable has to be connected to CN6

## Slide 13: Programming Arduino Processor from UDOO itself
Install Arduino 1.5.x on UDOO Ubuntu
J18 jumper should be plugged
Write the Arduino code
Upload the Arduino code

## Slide 14: i.MX6 & ATMEL

## Slide 15: Communication between I.MX6 & ATMEL SAM3X
/dev/ttymxc3

## Slide 16: Unidirectional communication from i.MX6 to Atmel Sam3x
Step1 – Serial Program for i.MX6
  Copy c_serial_example.c on UDOO rootfs
  Compile the application
    gcc c_serial_example.c –o c_serial_example
Step 2 – Create an Arduino project
  Remove the jumper J18
  Copy arduino_serial_example.ino on your host
  Create an Arduino project using Arduino IDE
  Compile & Upload the code
  Power off
  Put the jumper J18
Step 3 – Communication is ready
  Run ./c_serial_example

## Slide 17: Bidirectional communication i.MX6  Atmel Sam3x(I)
Step 1 – Update the Arduino Application(arduino_serial_example.ino)
  Reply to Linux Messages with various messages
    Serial.print
    Serial.println
Step2 – Update the Linux application (c_serial_example.c)
  Read the characters sent by Arduino and print
    read
Step 3 – Communication is ready
  Run ./c_serial_example
  Extra:
  Linux APP:
    Send commands to Arduino to switch off/on the in a given interval
      write

## Slide 18: UDOO Linux BSP

## Slide 19: Motivation
Linux is everywhere:
  800k phones, 700k TVs activated daily
  Google, Twitter, Facebook, Amazon
  9 out of 10 of the world's super computer
Open source
Top-notch programmers

## Slide 20: Linux Development Model
Open source:
  Competing companies work together: RedHat, IBM, Intel, Oracle, Nokia, HP, Google, etc.
Development model:
  Development cycle: 3 – 4 months
  Merge window: 2 weeks
Git trees:
  Official: Linus Torvalds
    git://git.kernel.org/pub/scm/linux/kernel/git/torvalds/linux-2.6.git
  Each important subsystem is maintained by a person
Notes: Notes:
http://kernelnewbies.org/UpstreamMerge

## Slide 21: General Architecture and Memory Layout

## Slide 22: General Architecture and Memory Layout
User Applications
Core Kernel Device Drivers
System API
Hardware
User Space
Kernel Space
3GB Virtual Memory
1GB Virtual Memory

## Slide 23: Kernel Space
Kernel Space

## Slide 24: User Space Interface
User and kernel modes have different privilege levels
Kernel Trap
Types: exceptions (divide error/page fault), syscalls.
Source: user, cpu, external interrupt
Handler: exception/interrupt table
Files
e.g. sysfs, debugfs, device files
Core Kernel Device Drivers
System API
Traps , Faults, System Calls
User
Kernel

## Slide 25: Hardware Interface
Hardware Interrupts
Memory-mapped I/O (/proc/iomem)
- same address space for memory and I/O
- request_mem_region, ioremap
Core Kernel Device Drivers
Hardware
Ports, Memory Mapped I/O, Interrupts

## Slide 26: Folder Structure
lxr.free-electrons.com

## Slide 27
Linux BSP and Configuration

## Slide 28: Linux BSP
Device Drivers
U-Boot
Linux Kernel
User’s
Apps
RFS

## Slide 29: U-Boot
Starts Kernel
What is U-Boot?
  universal bootloader
  open source firmware for hardware platforms
  a boot loader widely used in embedded space
      What does it do?
  brings the board to a sane state out of reset
  loads OS image onto board and starts OS
Reset vector points to SRAM
Begins execution in SRAM
Initializes UART
Checks info on version numbers, clocks
and displays on screen
Initializes DDR
Relocates itself to RAM
Continues execution in RAM
Initializes higher level devices :
Ethernet, SDHC, etc.
Begins command interpreter

## Slide 31: Root File System
The basic file system structure
Minimum set of directories: /dev, /proc, /bin, /etc, /lib, /usr, /tmp
Basic set of utilities: sh, ls, cp, mv, etc.
Minimum set of config files: rc, inittab, fstab, etc.
Runtime library to provide basic functions used by utilities

## Slide 32: Cross-Compiling

## Slide 33: U-boot Configuration
Load the Uboot UDOO configuration
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabi- udoo_dl_config/udoo_quad_config
Compile the uboot
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabi-
u-boot: uboot elf.
u-boot.imx: binary file with platform header.
System.map: symbol table file
Write the u-boot on the sd
sudo dd if=u-boot.imx of=/dev/<MICROSD_DEVICE_NAME> bs=512 seek=2

## Slide 34: Linux Kernel Configuration
Load the Kernel UDOO configuration
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabi- UDOO_defconfig
Modify default configuration
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabi- menuconfig
Compile the kernel
make ARCH=arm CROSS_COMPILE=arm-linux-gnueabi-
Device Tree Blob (.dtb) - only on Kernel 3.10 versions
vmlinux: kernel image with symbols
zImage: compressed and stripped kernel image
System.map: symbol table file